Complete word set

Word	Level	Description
+	0	Add B into A
.h	0	Display A on the screen in hexadecimal, prefixed by a space, at the current cursor position and move the cursor forward (low level debug output function)
0<	0	Set A to -1 if A <0, 0 otherwise
0=	0	Set A to -1 if A = 0, 0 otherwise
ab>r abc>r / r>abc r>ab / v>r r>v	0	Push and restore A, B, C or some combination to or from the return stack. Must unpick opposite – e.g. abc>r followed by r>abc must restore the abc registers.
c! !	0	8 and 16 bit writes of B to address A
c@ @	0	8 and 16 bit reads of address A into A
clr.screen	0	Clear Screen
cursor!	0	Set the cursor position to A
debug	0	Display A B C on the screen
halt	0	Stop, disable interrupts.
input@	0	Basic input device. Reads a word where the lower 5 bits are Fire Up Down Left Right active high (the same as a Kempston Joystick). The upper 11 bits are undefined as more buttons may become available.
port@ port!	0	Read and write Z80 ports
r1>r2	0	Copy r1 to r2 where rx is a b or c (not required if r1=r2)
screen!	0	Set the screen byte A to address B (2 + 6 bit)
swap	0	Exchange A and B
sys.info	0	Puts the address of the system info area into A after having copied A to B first.
wordsize*	0	Convert word count in A to overall byte size in A
-	1	Subtract A from B, result in A
0-	1	Negate A (2’s complement)
1+ 1- 2+ 2-	1	Adjust A by 1 or 2
abs	1	Set A to abs(A)
and or xor	1	Binary operator; A:= A <op> B
not	1	Not A (1’s complement)
> = < / >= <> <=	2	Compare A against B, set A to -1 if true, 0 otherwise
2* 4* 8* / 16* 256*	2	Shift A left
2/ 4/ 16/	2	Divide A by 2 and 4 and 16 (arithmetic not logical), note 222/ is part of the core set
max min	2	Set A to the larger or smaller of A and B
*	3	Multiply A by B, result in A
/	3	Divide A into B, result in A (unpredictable if A = 0)
bswap	3	Byte swap A
copy	3	Copy C bytes from B to A (copes with overlap)
fill	3	Fill C bytes from B with constant A
mod	3	Divide A into B, modulus of result in A